Controlled Delay (CoDel)
How it works
Simpler implementation
Implementation bugs (how it's meant to work?)
Design flaws
Unacknowledged prior work (incl. IPR)
Bob Briscoe
Aug 2012 – Oct 2021

---
Controlled Delay (CoDel)
How it works
Bob Briscoe
Aug 2012

---
queue evolution over time
assuming equal-sized packets for simplicity
drain rate
change
queue size
time
sojourn (service time)
of highlighted packet

---
CoDel target and interval
queue size
time
no drop during this interval because
(min within interval) < (target)
‘target’
sojourn
‘interval’ over which
CoDel takes minimum
interval hard-coded as a large global RTT (100ms)
target = interval / 20
due to a ‘universal rule’ yet to be written-up

---
at next dequeue CoDel drops packet
because (min > target)
queue size
time
target
drop because
min > target
min
sojourn
within
interval
‘interval’ over which
CoDel takes minimum

---
at next dequeue CoDel drops packet
because (min > target)
queue size
time
target
drop because
min > target
min
sojourn
within
interval
‘interval’ over which
CoDel takes minimum

---
predetermined drop sequence
once min > target
CoDel preordains the sequence of times that a packet will be dropped
until* min  target
although the algo
involves a square root,
the resulting (effective)
drop prob rises linearly
* every time a non-ECN pkt is picked, the queue will reduce by one.
After a round trip, the queue will reduce more, if the transport is responsive

---
CoDel
Alternative implementation of the control law
(despite believing the design is flawed – see later)
Bob Briscoe
Oct 2021

---
CoDel control law
alternative implementation{1}
unnecessary square root in design?
having calculated the drop probability, it grows linearly{2}
because the square root is multiplied by itself
this implies there should be a simpler implementation without approximating a square root
although I believe the design of the control law is flawed (it's disconnected from rate of queue growth)
I was intrigued enough to try to refactor the algorithm without changing its intent (time to drop_next = 1/√count)
{1}: although the existing approximation to a square root using one step of Newton's method is impressive
{2}: see earlier slide from Aug 2012

---
Alternative control law implementation
interval = I [s]
next_drop = D [s]
packet-rate = r [pkt/s]
count = n [pkt]
CoDel control law code:
        D(n) = I / sqrt(n)
Inst. drop probability:
        p(n) = 1/( r * D(n) )
Slope of rise in drop prob with time:
Δp/Δt = (p(n+1) - p(n)) / D(n)
        = (1/D(n+1) –1/D(n))/(r*D(n))
        = ( √(n(n+1)) - n ) / (r * I2)
At count = 1, the numerator starts at √2-1 = 0.414. As n increases, it rapidly tends to ½, i.e. nearly const.
So:
        dp/dt → 1/(2r*I2)
See my posting to aqm@ietf.org (12-Nov-2013)

---
Proved empirically
by Høiland-Jørgensen 07-Jun-2015
In response to posting on previous slide: source plot, expt definition

---
Alternative control law implementation
#define J_SHIFT 1
j = interval_pkts
j <<= J_SHIFT;
i0 = j * interval_pkts;
i = i0;
i0_sav = i0;
// for each packet
if (dropping) {
 i0++;
 i -= j;
 if (i < j) {
 j += i0 - i0_sav;
 i += i0;
 i0_sav = i0;
 // drop or mark packet
 }
}
Prep: count pkts in interval (interval_pkts), e.g. 1000
Initialize:
j = 2 * interval_pkts, e.g. 2,000
i = j * interval_pkts, e.g. 2,000,000
the algorithm counts i/j packets to next drop, by repeat subtraction, e.g. i/j = 1000 times
then increments both by this count, e.g.
j = 3,000
i = 2,001,000
so i/j = 667 to next drop
repeats 1&2 until queue below target, using same logic as CoDel (not shown)

---
Tested empirically
count [drop]
inter-drop interval [pkt]
error [%]
cf. Fidelity of Linux CoDel control law

---
CoDel
Caching control law state
How it works (or not, due to Linux bugs)
Bob Briscoe
Oct 2021

---
Summary of codel_dequeue() logic in Linux
(excluding ECN logic)
more efficient structure:
if (_drop) {
if (dropping) {…}
} else {
dropping = false;}
}
bool _drop = should_drop()
if (dropping)
if (!_drop)
dropping = false
else
if (now > drop_next)
while (dropping &&
      now > drop_next)
count++
Newton_step()
drop_func()
if (!should_drop())
    dropping = false
else
    drop_next = control_law()
else
if (_drop)
drop_func() // while (now>drop_next)?
_drop = should_drop()	// redundant?
dropping = true
_delta = count – lastcount
if ( (_delta > 1) &&	// >0 ?
   (now–drop_next < 16*interval) )
count = _delta	// count--; ?
Newton_step()
else
count = 1
rec_inv_sqrt = FFFF
lastcount = count
drop_next = control_law()

---
CoDel: potential problems
count-caching bugs in Linux
count wrongly set to delta on re-entering dropping mode
and if (delta > 1) should be (delta > 0)
AFAICT, when CoDel re-enters dropping mode:
if (count increased when last in dropping mode AND it's been <1.6s since last drop)
it should just use the count naturally stored when it last left dropping mode
but on this line, CoDel (code and RFC) inexplicably sets: count = (count – lastcount);
That is, the increase in count during the last period in dropping mode
(whether initialized to 1 or set to the cached value)
The problem: imagine entering dropping mode 4x in succession, and each time count reaches the value on the right (the clock icon ... indicates unnecessary delay):
Only an increase proves count is fresh so, instead of count = delta; I suggest:
count--; and if (delay > 0)
which is what the code effectively does the first time after count=1
delta	count	lastcount	...	count
	1	1	...	12
11	11	11	...	14
3	3	3	......	15
1	1	1	......	15

---
CoDel: potential problems
Other bugs in Linux codel_dequeue()
There should be a while loop around the drop() in the main else block,
to handle the case where a burst puts CoDel back into dropping mode
_drop = should_drop(); in the main else block is redundant,
because _drop is not stored and not used again
(remnant from a while loop?)

---
CoDel
Potential Design Problems
(from reading the code – to be proven)
Bob Briscoe
Apr 2013

---
CoDel: potential problems
lead-up to drop mode
CoDel completely suppresses any signal at all for ‘interval’
no matter how bad the queue has become
i.e. min() function depends wholly on one worst case, not the extent of worse cases
because a hard-coded interval is used,
it has to be based on the largest likely global RTT
for very short RTT (home network, ISP cache),
any congestion signal would be suppressed for perhaps hundreds of round trips
short RTT flows will exploit interval to take all the capacity
CoDel does not auto-tune any parameters, it hard-codes parameters
granted, the use of delay as a metric provides some inherent auto-tuning
the basis of hard-coded ‘target’ of 5ms is arbitrary
limit of human perception?
perceived delays typically made up of multiple rounds
queuing delay is per round
VJ says there is a ‘universally constant’ queuing delay at which there is a turning point in the power (bandwidth/delay)?
VJ has promised to write-up this ‘universal law’, but it’s TBA
this ‘universal law’ doesn’t apply at data centre rates though
to optimise bandwidth against delay depends on the utility of each, which is not linear with either bandwidth or 1/delay

---
CoDel: potential problems
control law in dropping mode
preordained rate of decrease of the interval between drops
drop is insensitive to how fast congestion grows
not a robust design, but specifically, it will take a very long time to bring the queue under control with unresponsive traffic (e.g. DoS attack)
in short, it is dependent on one specific transport behaviour,
contrary to RFC7567 Rec.4.5
no explanation for the square-root law has ever been forthcoming, except it's "related to the square root law of Reno" (?!)
precisely predictable drop times
a source may be able to game CoDel by synching on the first drop and avoiding the times when the next drop is due
using a timer selects the packet after it expires, and it's more likely to expire during a large packet
leads to bias against any small packet after a large packet (e.g. runt of a fragment pair){1}
ECN not disabled on overload{2}
If a packet is ECN-capable, Linux CoDel never drops it, even if severely overloaded, contrary to:
recommendation in Section 7 of [RFC3168]
SHOULD in Section 4.2.1 of [RFC7567]
which both recommend disabling ECN at high load
{2}: Oct 2021: Added
{1}: Oct 2021: replaced previous unfounded criticism of ECN retrofit with this more obvious flaw

---
sfq_anyAQM: potential problems
variable bit-rate real-time video
if bit-rate is close to capacity,
may add delay during bandwidth peaks
weighted flows e.g. within an rtcweb bundle
may force all flows into equal bit-rate
background flows, e.g. low weight TCP
may force all flows into equal bit-rate
if use fairly small #queues, sharded flows will collide with their worst enemies frequently, so either OK, or awful

---
(FQ_)CoDel Linux implementation
Priority ranked ToDo list
- Add ce_threshold_ect1 option
    - with slow link check for >1 packet
- Disable ECN at high load
    - sojourn > threshold?
- Make drop_next depend on queue length
    - either as well as or instead of count
- Include LSB of ECN field in FQ classifier
    - to prevent mixing of L4S and Classic within VPN

---
CoDel
reinventing many existing ideas
we should use this experience
Bob Briscoe
Apr 2013

---
relevant publications
[PDPC03] M. Sågfors, R. Ludwig, M. Meyer, J. Peisa, (Ericsson) “Queue management for TCP traffic over 3G links”in Proc. IEEE Wireless Communications and Networking, Mar 2003
[PDPC+03] M. Sågfors, R. Ludwig, M. Meyer, J. Peisa, (Ericsson) “Buffer Management for Rate-Varying 3G Wireless Links Supporting TCP Traffic,” In Proc Vehicular Technology Conference, Apr 2003
[PDCP08] 3GPP TS 36.321. E-UTRA; Medium Access Control (MAC) protocol spec, v8.2.0. May 2008; early drafts:
“SDU Discard” R2-074689, 12 Nov 2007
“Specifying SDU Discard Function for the UE” R2-074703, 12 Nov 2007
[TSG-AQM08] 3GGP R2-080937, On the Need for Active Queue Management for non-GBR Bearers, TSG-RAN WG2 Meeting #60bis, February 2008

---
relevant patent families
[Eric01] Congestion and delay handling in a packet data network
EP 1 391 128, EP 1 876 779 , US 2004 218617
Priority: 31-May-2001
Assignee: Ericsson, SE
Status: ?
[Qual06] Method And System For Reducing Backhaul Utilization During Base Station Handoff In Wireless Networks
WO 2008 070713, EP 2 127 256, US 2008 186918
Priority: 05-Dec-2006
Assignee: Qualcomm Inc
Status: EU: exam’n in progress, US: ready for exam’n
[Fuj09] Packet Buffering Device and Packet Discarding Method
US 2011 0286468
Priority: 6 Feb 2009
Assignee: Fujitsu, JP
Status: US: under exam’n
[Eric09] AQM for Wireless Communication Network Uplink
EP 2 409 516, US 2012 039169
Priority: 20 Mar 2009
Assignee: Ericsson, SE
Status: EU: granted 13-Mar-2013, US: under exam’n

---
summaries
[PDPC03]: (Packet Discard Prevention Counter) A deterministic (not random) algo drops a single packet then allows n packets (or bytes), if the instantaneous (not averaged) queue exceeds a threshold in units of bytes. Both ideas are used in CoDel to reduce signalling delay.
[PDPC+03]: Extension of PDPC that adapts the threshold (in bytes) dependent on the local link rate.
[Eric01]: Ericsson patent on the suppressing discard for n packet (or bytes) after a single discard, which CoDel seems to infringe
[PDCP08]: Adopted in 3GPP E-UTRA MAC spec.
Simple AQM algo that discards packets when queuing delay exceeds a threshold. Outcome: sacrifices throughput for low delay
[TSG-AQM08]: Proposal not adopted by 3GPP.
Delay-based AQM that avoids consecutive drops
[Qual06]: Includes delay in a list of metrics that could be used as the threshold for AQMs. Insufficiently detailed description of any delay metric mechanism to be able to infringe?
[Fuj09]: Predicts queuing delay at the future time when the packet that is currently arriving departs, in order to drop arriving packets if the prediction exceeds a threshold. Optionally also drops from the head of the queue if actual queuing delay exceeds a threshold, but does not claim this as novel. Describes measuring the queuing delay as the difference between arrival and departure times. Only describes this last aspect, doesn’t claim it, but still under examination phase, so a claim could be added, which CoDel would seem to infringe (but it may be judged obvious).
[Eric09]: eNodeB (base station) implements AQM for the uplink based on queue delay in the user equipment (UE). Covers the more general case of an AQM on one node dropping on behalf of a queue on another node. Unlikely to be infringed by the way CoDel does this.