## Slide 1: Internet Architecture Board; Report Back
IAB Stack Evolution Programme: interaction with NFV
Doc: TBA
Source: Bob Briscoe, BT
Agenda item: Liaisons
For: Discussion
© ETSI 2015. All rights reserved

## Slide 2: IAB Stack Evolution Programme
Internet Architecture Board (IAB)
  Architecture and Liaison activity for the IETF
IAB Stack Evolution Programme
  Addressing near-impossibility of evolving the Internet stack
This talk
  Prepared in co-operation with our IETF liaison: Diego Lopez
  Recent IAB workshop: Stack Evolution in a Middlebox Internet (SEMI) <https://www.iab.org/activities/workshops/semi/>
    participants decided to reach out to NFV ISG
    this update is given in my personal capacity
  More formal liaison or joint action could follow

## Slide 3: Collision course
Pervasive monitoring by government agencies
  Snowden revelations
The middlebox tussle
  two perceived drivers: security protection & business protection
  widespread blocking of IETF extensibility mechanisms
    new e2e protocols (IP next header numbers) blocked, e.g. SCTP
    new services (port numbers) blocked (often leaving only https and http)
    new protocol option numbers blocked (e.g. TCP options like multipath)
IAB/IETF response in both cases:
  plans to encrypt and authenticate all end-to-end protocol fields and data
    protects privacy*
    enforces architecture
  unsolicited services might be useful, but they have no right to data visibility
* Nov 2013 IAB recommendation to harden Internet Confidentiality
Notes:     Blocking extensibility:
    1. Slows introduction of new OTT competition a little
    2. Reduces the attack surface a little
    But:
    1. merely shifts new services to within http (over the top of the top)
    2. merely shifts attacks to within http

## Slide 4: Impact
Market in (virtualised) network functions could shrink
Need to define new interface(s)
    need to shift from unsolicited to solicited intervention
    signalling from app to network function, or vice versa
    in-band preferred, out-of-band maybe
    think "ICMP that works"
ICMP: Internet Control Message Protocol

## Slide 5: Potential positive role of NFV recognised
freshness – protocol extensions should deploy faster
  protocol extension often not possible with hardware middleboxes
  more systematic update practices as NFV becomes the norm
a voice for the middlebox industry
  NFV ISG brings most middlebox vendors and operators together
  the first time the IETF can address this industry in one place
Downsides also recognised
staleness
  many virtual appliances will still be updated rarely or never
not central to scope of NFV ISG
  data plane interfaces specific to each network function
  (but security ToR does address pervasive encryption)

## Slide 6: Next steps
Invitation to relevant IETF activities
  IETF WGs: httpbis, TAPS, tcpinc, TLS, tsvarea, PCP, ...?
  non-WG mailing list: Handling pervasive monitoring (PERPASS)
  Potential activities: MCIC, SPUD, middlebox detection & error collection, ...?
  Collectively forming decisions on
    trust model
    crypto coverage in protocol headers
  next IETF meeting, Dallas 22-27 Mar 2015.
IAB stack evolution programme*
  lead: Brian Trammel
NFV ISG activity?
joint NFV-IETF initiative?
TAPS: TrAnsPort Services
tcpinc: TCP INCreased security
TLS: Transport Layer Security
tsvarea: Transport Area Plenary
PCP: Port Control Protocol
MCIC: Multiparty Content Integrity & Confidentiality
SPUD: Session Protocol Under Datagrams
  * <https://www.iab.org/activities/programs/ip-stack-evolution-program/>