## Slide 1: Prague requirements survey based on draft-ietf-tsvwg-ecn-l4s-id-12 updates in draft-ietf-tsvwg-ecn-l4s-id-14
  Koen De Schepper, Nokia Bell Labs
Bob Briscoe, independent
TSVWG @ IETF110
March 9, 2021

## Slide 2: Survey for Prague Congestion Controls
Goal: are Prague requirements feasible/realizable and supported by a broad community (allows several different CCs)?
Template provided:
  List of all normative requirements
  List of 3 performance improvement suggestions (no normative text)
Targeting Congestion Control developers having a Prague CC, or that plan to support L4S using the L4S-ID ECT(1)
2 questions asked:
Compliant / Partially Compliant / Non-compliant Explain at what level you (plan to) meet the requirement | Any description/limitations/remarks/explanation related to evaluation, implementation and plans (will implement or will not implement) can be explained here. Any expected or experienced issues and any objections/disagreements to the requirement can be explained and colored appropriately here.

## Slide 3: Multiple responses received
3 were publicly shared:
Linux TCP-Prague by L4Steam
SCReAM by Ingemar Johansson
GeforceNow by NVIDIA
 Listed in https://l4steam.github.io/#prague-requirements-compliance
Other responses shared privately:  consolidated summary available at:
https://l4steam.github.io/PragueReqs/Prague_requirements_consolidated.pdf

## Slide 4: Compliant/supported or planned by all
Requirements:
An L4S sender MUST set the ECN field to ECT(1)  OS APIs and Kernels need to support it
MUST NOT set ECT(1) unless it complies with …
A sender that sets ECT(1) SHOULD implement a scalable congestion control
MUST provide feedback of the extent of CE marking …  Some remaining concerns with Accurate ECN  tcpm
MUST reduce RTT bias …  Also, more throughput is planned for longer RTTs
SHOULD detect loss by counting in time-based units …
Non-Normative performance suggestions:
Setting ECT(1) in TCP Control Packets and Retransmissions
Faster than Additive Increase
Faster Convergence at Flow Start
Actions on the draft:
 OK after minor clarifications

## Slide 5: Strong objections on documentation-only reqs
The specification MUST describe in detail …
The specification MUST define, quantify and justify burst limit approach …
- Are these documentation requirement really needed? - How can it be enforced? - May not be possible (proprietary).
Actions on the draft:
 These requirements have been removed

## Slide 6: Needs experimental data
SHOULD scale down to fractional congestion window …
Not all convinced if it will be a problem on the Internet, and might not implement
Multiple research implementations exist; others support it or plan to implement
 Not a safety issue, but would prevent extra latency on L4S-only queues and drop on Coupled-AQMs  Propose: Keep SHOULD. Develop further during experiment as needed.
Actions on the draft:
 Updated based on discussions on the mailing list (further refinement/clarifications)

## Slide 7: Needs experimental data
MUST implement monitoring to detect non_L4S ECN AQM…
Is detection itself required?
Robust detection scheme needs real deployment experience.
Combination with delay-based control could minimize potential issues
Develop during experiment as needed.
SHOULD be capable to automatically fall back …
MUST be capable of being replaced (operator action) by a Classic congestion control …
Is “replace” required or can it disable L4S part to reduce to Classic response only
On active flows or new flows
 If L4S Operational guidelines draft is adopted, these requirements will need to be aligned with it.
Actions on the draft:
 Todo: further refinement/clarifications

## Slide 8: Compliant (to intent) by all: Needs Clarification
MUST react to packet loss in a way that will coexist safely with a TCP Reno congestion control [RFC5681] …
Not clear what it means "coexist safely with a TCP Reno congestion control“
Don't want to be as degraded as Reno for long RTTs
 Seeking input from WG on correct wording for this requirement e.g. RFC5033
 Discussion started on the mailing list
Balance between openness to innovations and guidance/recommendations
  keep open during experiment, not the mechanism but the result is important
  Practical example in TCP-Prague CC draft

## Slide 9: Conclusion
Strong objections against “MUST document”  all removed
Develop during experiment to determine need and get real live data:
  Scaling down to fractional windows
  Classic ECN bottleneck detection  align with L4S-ops if adopted
Others already have implementations, or req’s are seen as feasible and are planned to be implemented
Other inputs are still welcome (public or private)

## Slide 10: Backup

## Slide 11: All agreed: Compliant or planned
An L4S sender MUST set the ECN field to ECT(1) | - Compliant or planned - OS APIs and Kernels need to support it (can RFC8311 be used to justify API updates) | None, OK as is
A sender that sets ECT(1) SHOULD implement a scalable congestion control | - Compliant or planned - More clarification needed to align marking rate to throughput | Improve informative text for rate convergence of long flows
MUST eliminate RTT … | - Compliant or planned - Also for longer RTTs more throughput is planned | None, OK as is
SHOULD detect loss by counting in time-based units … | - Compliant or planned | None, OK as is
MUST NOT set ECT(1) unless it complies with following … | - Compliant to this requirement - Comments were on referred requirements | None, OK as is

## Slide 12: All agreed (non-normative): Supported or planned
Setting ECT(1) in TCP Control Packets and Retransmissions | - Supported or planned | RTP/RTCP clarifications will be added
Faster than Additive Increase | - Supported or planned | None, OK as is
Faster Convergence at Flow Start | - Research code exists and planned | None, OK as is

## Slide 13: Questioned and Strong objections
The specification MUST describe in detail … | - Is this requirement really needed? - How can it be enforced? - May not be possible (propriatary). | This requirement is removed
SHOULD scale down to fractional congestion window … | - Multiple research codes exist - Not all convinced if this is needed, others support it and plan to implement - Develop during experiment as needed. | Keep SHOULD. The need for this requirement should be observed during the experiment
limit bursts … The specification MUST define, quantify and justify its approach … | - Normative requirement is mainly documentation related, see above - Can more clear guidelines be given? | The normative MUST is removed. Warning text still present.

## Slide 14: Clarification needed
MUST provide feedback of the extent of CE marking … | - Compliant - Clarification needed for feedback timing and RTT requirements - Some remaining concerns with Accuate ECN | - Appropriate feedback timing depends on the proprietary protocol and needs to be tuned to it - Remaining concerns about Accurate ECN needs to be dealt with in tcpm.
MUST react to packet loss in a way that will coexist safely with a TCP Reno congestion control [RFC5681] … | - Compliant to the intent - Not clear what it means "coexist safely with a TCP Reno congestion control" - Don't want to be as degraded as Reno for long RTTs | - Seeking input from WG on clarification to this requirement e.g. RFC5033
MUST implement monitoring to detect non_L4S ECN AQM… SHOULD be capable to automatically fall back … MUST be capable of being replaced by a Classic congestion control … | - Robust detection scheme needs real deployment experience. - Develop during experiment as needed. - Combination with delay-based control could minimize potential issues - Clarification: is detection itself required? | - If L4S Operational guidelines draft is adopted, these requirements will need to be aligned with it