Accurate ECN Feedback for TCP
(AccECN)
Bob Briscoe, Independent	<ietf@bobbriscoe.net>
Feb 2023
[Speaker Notes: Cover Slide 1 of 3 Cable Labs]

---
TCP Congestion Feedback
Background & Problem
- L4S repurposes standard Explicit Congestion Notification (ECN) [RFC3168]
    - which "marks" more packets in the IP header (v4 & v6), the greater the queue.
- L4S sender keeps delay v low by adjusting rate in response to extent of these marks
    - reported via end-to-end transport layer feedback
- Works fine with feedback in modern transports like QUIC, DCCP or RTCP
  [RFC9000, RFC4340, RFC8888]
- ...but TCP was only designed to feed back existence not extent of congestion
    - sufficient when ECN was added back in 2001 [RFC3168]

---
Accurate ECN TCP feedback
draft-ietf-tcpm-accurate-ecn
- AccECN reuses the 3 ECN flags in the main TCP header (ACE)
    - 3-bit counter to feed back number of IP-ECN marks
    - also to negotiate support by both TCP ends during the handshake
- AccECN TCP Option
  optionally adds wider counters
  that won't wrap
- Planned Proposed Standard
  generic TCP wire protocol
    - also supports non-L4S behaviours
- IETF WG last call Mar'23
- Implemented in Linux (being maintained by Google), FreeBSD & Apple OSs (in progress)
Main TCP header
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typical 5-8B, max 11B
TCP Options...