## Slide 1
Bob Briscoe, Independent <ietf@bobbriscoe.net>
Feb 2023
Accurate ECN Feedback for TCP (AccECN)
Notes: Cover Slide 1 of 3
Cable Labs
<number>

## Slide 2
TCP Congestion Feedback Background & Problem
L4S repurposes standard Explicit Congestion Notification (ECN) [RFC3168]
    which "marks" more packets in the IP header (v4 & v6), the greater the queue.
L4S sender keeps delay v low by adjusting rate in response to extent of these marks
    reported via end-to-end transport layer feedback
Works fine with feedback in modern transports like QUIC, DCCP or RTCP [RFC9000, RFC4340, RFC8888]
...but TCP was only designed to feed back existence not extent of congestion
    sufficient when ECN was added back in 2001 [RFC3168]

## Slide 3
Accurate ECN TCP feedback draft-ietf-tcpm-accurate-ecn
AccECN reuses the 3 ECN flags in the main TCP header (ACE)
    3-bit counter to feed back number of IP-ECN marks
    also to negotiate support by both TCP ends during the handshake
AccECN TCP Option optionally adds wider counters that won't wrap
Planned Proposed Standard generic TCP wire protocol
    also supports non-L4S behaviours
IETF WG last call Mar'23
Implemented in Linux (being maintained by Google), FreeBSD & Apple OSs (in progress)
00 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 20 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 30 | 1
Port no’s, Seq no’s... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data Offset |  |  |  | Res-erved |  |  | ACE |  |  | URG | ACK | PSH | RST | SYN | FIN | Window |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Checksum |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Urgent Pointer |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TCP Options... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
AccECN Option, length: min 2B, typical 5-8B, max 11B |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TCP Options... |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Main TCP header