Accurate ECN Feedback for TCP (AccECN)
draft-ietf-tcpm-accurate-ecn
Bob Briscoe, Independent
Mirja Kühlewind, Ericsson
Richard Scheffenegger, NetApp
TCPM WG, IETF-116, Mar 2023
[Speaker Notes: Cover Slide 1 of 3 Cable Labs]

---
TCP Congestion Feedback
Background & Problem
- DCTCP, L4S etc. repurpose standard ECN [RFC3168]
    - which "marks" more packets in the IP header (v4 & v6), the greater the queue.
- Sender keeps delay v low by adjusting rate in response to extent of marks
    - reported via end-to-end transport layer feedback
- Works fine with feedback in modern transports like QUIC or DCCP
  [RFC9000, RFC4340]
- ...but TCP was only designed to feed back existence not extent of congestion
    - sufficient when ECN was added back in 2001 [RFC3168]

---
Accurate ECN TCP feedback – recap
draft-ietf-tcpm-accurate-ecn
- AccECN reuses the 3 ECN flags in the main TCP header (ACE)
    - 3-bit counter to feed back number of IP-ECN marks
    - also to negotiate support by both TCP ends during the handshake
- AccECN TCP Option
  optionally adds wider counters
  that rarely wrap
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typical 5-8B, max 11B
TCP Options...

---
Recent changes (Nov'22 → Feb'23)
draft-ietf-tcpm-accurate-ecn-22 → 23
- Unclear areas found during Apple implementation:
    - Use handshake encoding also for pure ACK of any retransmitted SYN/ACK
    - detection and response to pure ACK loss due to the AccECN TCP Option
      (symptom would be continual retransmissions)
- Fixed "idnits" and some other minor editorial issues

---
Recent changes 1/2 (Feb'23 → Mar'23)
WG last call 7 Mar – 24 Mar 2023
- Review from Michael Tüxen: all resolved – largely editorial
  [archive 8 Mar 23]
    - additionally defined position of TCP header flags using same bit offset terminology as IANA
    - specified big-endian for option counters and LSB for the ACE field
    - s/IP header/TCP header/ (whoops!)
    - Clarified requests to IANA; asked for the ExID assignments to refer to the RFC-to-be
- Editorial issue from Alex Burr resolved
    - two occurrences of 'experiment' missed [github issue #4]

---
Recent changes 2/2 (Feb'23 → Mar'23)
- Review from Gorry – all editorial [archive 25-26 Mar]
    - Checking 'actor' in each req't: Data Sender, Data Receiver, host, TCP Client, TCP Server, 'it'
    - Promote §3.3 on requirements for Proxies, Offload & Other Middleboxes to §4?
    - Numerous other useful improvements
- Review from Markku [archive 26 Mar]
    - Describe how IANA would allocate remaining bit combinations?
    - Forward compatibility: only treat all other combinations of 3 header flags as AccECN...
      if not otherwise understood
    - ACKs of pure ACK: only relevant to ECN++ draft (EXP) so shift this text there?

---
AccECN Implementations
- Linux (v5.15)
- FreeBSD (except AccECN TCP Options)
- Apple OSs (in progress)

---
Next Steps
- draft-ietf-tcpm-accurate-ecn-23 → 24
    - in progress
    - to address all the WGLC reviews
- Thank you