Accurate ECN Feedback for TCP (AccECN)
draft-ietf-tcpm-accurate-ecn
Bob Briscoe, Independent*
Mirja Kühlewind, Ericsson
Richard Scheffenegger, NetApp
TCPM WG, IETF-117, Jul 2023
* Bob Briscoe's recent work on this document has been funded by Apple Inc.
[Speaker Notes: Cover Slide 1 of 3 Cable Labs]

---
TCP Congestion Feedback
Background & Problem
- DCTCP, L4S etc. repurpose standard ECN [RFC3168]
    - which "marks" more packets in the IP header (v4 & v6), the greater the queue.
- Sender keeps delay v low by adjusting rate in response to extent of marks
    - reported via end-to-end transport layer feedback
- Works fine with feedback in modern transports like QUIC or DCCP
  [RFC9000, RFC4340]
- ...but TCP was only designed to feed back existence not extent of congestion
    - sufficient when ECN was added back in 2001 [RFC3168]

---
Accurate ECN TCP feedback – recap
draft-ietf-tcpm-accurate-ecn
- AccECN reuses the 3 ECN flags in the main TCP header (ACE)
    - 3-bit counter to feed back number of IP-ECN marks
    - also to negotiate support by both TCP ends during the handshake
- AccECN TCP Option
  optionally adds wider counters
  that rarely wrap
00	1	2	3	4	5	6	7	8	9	10	1	2	3	4	5	6	7	8	9	20	1	2	3	4	5	6	7	8	9	30	1
Port no’s, Seq no’s...
Data Offset				Res-erved			ACE			URG	ACK	PSH	RST	SYN	FIN	Window
Checksum																Urgent Pointer
TCP Options...
AccECN Option, length: min 2B, typical 5-8B, max 11B
TCP Options...

---
Recent Process History
- 24 Mar-23: 3-week WGLC #1 ended
- 30-Mar-23: draft-24 closed off WGLC issues
    - except waiting for Markku's response
- 24-May-23: Draft editor channelled 2 offlist issues to list
- 26-May-23: Markku's follow-up comments
    - mid-Jun-23: resolved or shifted text to ECN++ draft
- 30-Jun-23: Solutions to offlist issues all posted; no objections
- 10-Jul-23: Markku's repeat follow-up
    - response 22-Jul-23: see later slide
- 24-Jul-23: draft-25 (editorial Δs) and draft-26 (technical Δs) posted to close off WGLC#1
    - draft-25: editorial tidy up: consistency & moved 2 general req's from over-specific sections
    - draft-26: technical / normative issues resolved (?) – see following slides

---
Recent changes 1/6
draft-ietf-tcpm-accurate-ecn-25 to -26
- Markku Kojo's follow-on review [archive 26-May-23 1,2]
- Situation as of draft-24:
    - increment-triggered ACK rule:
      "Receiver MUST ACK 'n' CE marks" (including on ACKs)
      - even tho' ECN-capable ACKs are not stds track
      - for completeness and as mechanistic reflector
    - Only happens if sender makes pure ACKs ECN-capable
      - then conditional on SACK-negotiated, so that sender can distinguish non-SACK DupACKs
- Sender-side shifted out of AccECN spec to ECN++ (exp-track)
    - and generalized 'ECN++' to any RFC for ECN-capable TCP control packets
- Markku: Still potentially drags a stds-track receiver into experiments ack'ing ACKs
- Response: as a necessary generic stds-track receiver, not experimental
    - Analogy: experimental congestion controls use a generic stds-track TCP receiver

---
Recent changes 2/6
- Michael Tüxen as doc shepherd [archive 29-Jun-23]:
    - -24 Intro: AccECN RECOMMENDED to be implemented alongside SACK and ECN++
      - SACK is useful, but not essential
      - ECN++ benefits are not specific to AccECN
    - -25: AccECN RECOMMENDED to be implemented alongside SACK; TSopt can be useful
      - refs to SACK & TSopt made normative
      - moved ECN++ support text to §5.2 on compatibility with common options and current experiments

---
Recent changes 3/6
- Draft editor (offlist), with Wes Eddy's help
    - Generalized definition of 'acceptable packet' to work round IPR on RFC5961:
      ...passes tests in RFCs 9293 & 5961, or other tests with equivalent protection
- Draft editor [archive 19-Jun-23]
    - §3.1.3 Forward Compatibility: what AccECN does:
      - on receipt of any of the 5 reserved SYN combinations
      - but not on receipt of the reserved SYN/ACK combination
    - answer: treat as if negotiating AccECN
      - and consider that it feeds back that the IP/ECN field
        on the SYN was unchanged

---
Recent changes 4/6
- Unclear text found during Apple implementation [archive 19-Jun-23]:
- Handshake interaction with Classic ECN is fine, but fall-back to non-ECN lacks details (just says "based on RFC3168", which lacks details too)
    - Moved a couple of rules buried in over-specific sections:
      - if receive re-xmt of SYN or SYN/ACK, feed back the most recent IP-ECN field
      - after a feedback mode is entered, MUST NOT switch
    - Added example sessions and following general rules (§3.1.5):
      - a Server in AccECN feedback mode
         SHOULD emit AccECN SYN/ACK in response to non-ECN SYN
      - a Server in Non-ECN feedback mode
         SHOULD emit Non-ECN SYN/ACK in response to AccECN SYN
      - a Server in AccECN feedback mode
         MUST NOT set ECT, if it has received or sent a non-ECN SYN or SYN/ACK
    - Any AccECN implementation
      - SHOULD ignore TCP/ECN flags on SYNs & SYN/ACKs arriving after it's synchronized
    - Resulting rules checked against numerous patterns of loss & delay during handshake
A
B
TCP
IP
Mechanistic
feedback
CCA
CCA
ECT?
ECT?
Other half
connection

---
Recent changes 5/6
- Draft editor [archive 30-Jun-23]:
    - 2 sections conflict: MUST/SHOULD test for zeroing of ACE field
      - §3.2.2.1: MUST test ACK of SYN/ACK:
      - §3.2.2.4: SHOULD test initial SYN=0 packet in either direction
    - Solution:
      - Exclude handshake packets from scope of latter section
      - Then 'SHOULD' → 'MAY' in latter section
        (if no zeroing during handshake, unlikely to be zeroing afterwards)

---
Recent changes 6/6
- IANA: TCP Option kinds [7 Nov 22]:
    - IANA assigned WG chair request: 172 & 174 (0xAC & 0xAE)
    - Error #1: I (BobB) wrote 172 & 173 into draft-22
    - Error #2: including the notes for IANA to publish about changing from experimental values
    - IANA faithfully copied these notes back to their experimental assignments page
- IANA noticed Error #1 [21 Jul 23]
    - implementations all (fortunately) followed IANA response: 172 & 174
    - draft-26 now fixed to match main IANA page: 172 & 174
    - editor notified IANA of Error #2 & IANA page fixed

---
Implementations status
- Apple client OS's [Vidhi Goel]:
    - AccECN TCP beta released 6 Jun'23 (off by default)
    - Developer resources: developer.apple.com/videos/play/wwdc2023/10004/
- FreeBSD [Richard S]
    - 14.0 reviews.freebsd.org/D21011
    - Plan to add AccECN TCP Options after 14.0 release reviews.freebsd.org/D36303
- Linux [Ilpo Järvinen, Neal Cardwell, Chia-Yu Chang]
    - against v5.15: github.com/google/bbr/commits/l4s-testing-2023-02-23-v3
      github.com/L4STeam/linux/blob/testing/README.md
    - mainlining in progress
    - RaspOS [Rob McMahon]
- Tools:
    - wireshark, packetdrill, tcpdump (wip) [Michael Tüxen, Richard S, Neal C, Vidhi G]

---
Next Steps
- This completes WGLC#1
- WGLC#2 after this meeting
- Thank you